## Slide 1: NVMeDirect: A User-Space I/O Framework for Application-specific Optimization on NVMe SSDs
Papers
  Hyeong-Jun Kim, Young-Sik Lee, Jin-Soo Kim
  The 8th USENIX Workshop on Hot Topics in Storage and File Systems (HotStorage), 2016
Motivation and Solution
  General scheme: User Apps -> VFS/File System -> Block Layer -> NVMe Driver -> NVMe SSD
   there are overheads occurred by storage stack layers
  New Scheme: User Apps -> NVMeDirect Framework(NVMe I/O Queue) -> control/data
  NVMeDirect
    Allows user-space applications to directly access NVMe SSDs without any hardware modifications
    Support various I/O policies
    Designed to maximize performance for trusted applicatioins
  Advantage
    Enable high performance I/O
    Easy to support new interfaces and develop and debug
    Provide various I/O policies
  Conclusion
    First full frame work for I/O in the user-space based on stock NVMe devices
    Can be easily applied to many applications
    Useful for emerging storage device

## Slide 2: MQSim: A Framework for Enabling Realistic Studies of Modern Multi-Queue SSD Devices
Papers
  Arash Tavakkol, Juan Gomez-Luna, Mohammad Sadrosadati, Saugata Ghose, Onur Mutlu
  The 16th USENIX Conference on File and Storage Technologies (FAST), 2018
Motivation and Solution
  Major feature missing in most existing simulators
    Multi-queue protocols
    Steady-state behavior: difficult to reach steady state in most simulators / Very slow, widely-used trace are not large enough
    End-to-end request: operations which occurred near flash do not have big overhead
  Major features of MQSim
    Accurately models conventional STA-based SSD and modern MQ SSDs
    Flexible design
    Open source
  How to solve the challenges?
    Support to types of mode according to SSD policy
    Preconditioning -> show similar performance with real SSD
  MQSim is highly accurate!!